## Slide 1: MAXQ7653 – MAXQ7660 (UC21)
SP&C Micro-Controllers + Analog = Intelligent Analog
  David Voutour
  Niraj Kumar
  Mike Mellor
  Anita Ganti

## Slide 2: SP&C Micro-Controllers
BU goal to address a market of $700M and achieve a revenue of $97M/yr with uC’s (Analog + Microcontrollers = Intelligent Analog) in the next 5 years (Focus on the Automotive, Industrial, Medical Electronics end-markets).
Launch at the rate of at least 2 product families a quarter
Historically focused on fast, 8051 drop-in-compatible, and secure µCs - Current Focus – MAXQ RISC based C Cores:
  RISC 8-bit & 16-bit Maxim-Dallas uC Cores
Future:
  DSPs

## Slide 3: MAXQ765X–automotive dgn guide

## Slide 4: MAXQ765X–data sheet

## Slide 5: Target Markets
Applications -10-bit/12-bit SAR ADC, uC with CAN and/or LIN
  Automotive
    Electronic Power Assist Steering
    Memory Seats and Anti-pinch Seat Control
    Dashboard Electronics
    Body Control Systems
    Industrial/Automotive Sensors
    Tire pressure sensing
    Adaptive Anti-collision Cruise Control
Electronic Power Steering

## Slide 6: Target Markets
Applications (10-bit/12-bit SAR ADC, uC with CAN and/or LIN )
  Automotive
    Vehicle Battery Monitoring
    Vehicle Exhaust Monitoring
    Vehicle Instrument Cluster Control
Dashboard Control
Intelligent Battery Monitoring

## Slide 7: Target Markets
Applications (10-bit/12-bit SAR ADC, uC with CAN and/or LIN )
  Industrial
    Valve Controller
    Building Automation
    Elevator Control
Industrial Flow Control
Pressure Transducer Module

## Slide 8: Target Competition & Share
Notes:   Maxim 14.08%
  Microchip 18.51%
  TI 7.55% - Not a serious automotive player – lack MSP430 & CAN
  ADI 3.26% - Not a serious automotive player – lack CAN (Targeting industrial, optical and automotive support with LIN)
  Micronas 9.10%
  Mot/Freescale 9.10% Not yet offering analog intensive automotive uC’s
  Philips 0.30%
  ASIC 9.12%
  Other 27.54% (ST, Hitachi, Mitsubishi, Uc+ADC, othet players changing direction)
  Cygnal/Si Labs 1.45%

## Slide 13: (UC21) MAX7653 – MAXQ7660
  High Performance, 16-bit RISC Microcontroller
  32 / 64 / 128kByte Program / Data FLASH
  MASK Program ROM Available
  1 or 2kByte Internal Data RAM
  On-Chip JTAG Download / Emulation / Debug Support
  8MHz Maximum Clock Frequency (ext XTAL or internal FLL), Also 2nd 32k XTAL for Low-Power Operation
  +5V and +3V Versions (internal core always +3V)
  Very Low Power (FLASH: < 2.5mA/MIPS at +3.3V, MASK ROM: <1mA/MIPS at +3.3V)

## Slide 14: UC21 – MAX7654 – MAXQ7658
  3 Brownout Voltage Monitors (DVDD, AVDD, VDDIO)
  Low-Power, 16-Channel, 12-bit, 500ksps ADC
  Dual, 12-bit, Buffered, Force/Sense DACs
  Low-Power Op Amp
  Internal Voltage Reference (independent DAC and ADC ref)
  Local (Die) / Remote Transistor Temperature Sensing

## Slide 15: UC21 – MAX7654 – MAXQ7658
  CAN2.0BTM Interface (up to 1Mbps)
  4-Wire SPITM Serial Interface
  Four 16-bit (or eight 8-bit) Timer / Counter / PWMs
  22 Digital I/O (many muxed; all are interrupts / wakeups)
  16x16, 1-cycle, HW Multiply with 48b Accumulate
  -40°C to +85°C / +125°C Operating Temperature Range
  56-Pin (8mmx8mm), and (future) 68-Pin QFN Packages
  SAMPLES OCTOBER 2004

## Slide 16: A/D Detailed Block Description
  A/D Converter, Temperature and Supply Voltage Measurement
  12-bit ADC capable of converting at rates as high as 500ksps.
  16 single-ended inputs (relative to AGND), or up to 8 fully differential inputs.
  unipolar and bipolar modes with respective input ranges of 0V to REFADC, and –REFADC / 2 to +REFADC / 2.
  supports local (die) temperature measurement,
    dual remote diode-connected transistor temperature measurement
    built-in AVDD measurement capability
    Optional to use AVDD as its reference voltage allowing ratiometric measurements proportional to the AVDD supply.
  A/D input signal tracking (acquisition), sampling, and conversion can be controlled via the following methods:
    Software register bit writes
    Continuous conversions (16 ADCCLK cycles)
    Internal Timers (T0, T1, T2, or T3)
    External Pin (P0.4_ADCCTL)

## Slide 17: D/A Detailed Block Description
  D/A Converters
  12-bit, dual, force / sense DACs that settle within 8us typically and 15us max.
  Unity gain (with no external components) and rail-to-rail output (with external components) options.
  Absolute output with respect to internal 2.048V/4.096V or external reference.
  Ratiometric outputs with AVDD as reference.
  Each DAC has double buffered input registers for simultaneous update
  Toggle mode between 2 DAC output levels (programmable square wave generator)

## Slide 18: CAN Detailed Block Description
    CAN2.0B Interface
    Programmable bit rates from 10kbps to 1Mbps
    15 message centers (14 Tx or Rx, 1 Rx only with FIFO)
    11-bit standard or 29-bit extended identifiers
    SIESTA low-power mode
    Wakeup on CANRX edge transition (1st associated CAN message not captured.)
    Disables transmitter during autobaud
    Supports DeviceNET, SDS, and higher level CAN protocols

## Slide 19: Product Dev. Support
  Product Development Support
    In-Circuit Emulator
    EV-kit October 2004
    Software Development Libraries
    Applications Support

## Slide 20
Host Development Computer
INTEGRATED DEVELOPMENT
ENVIRONMENT

## Slide 21
PRODUCT EMULATOR

## Slide 22: EV-Kit Description
  Flexible Power Supply Configurations
  Built-in adjustable supplies (AVdd, DVdd,Vddio) for supervisor testing
  SPI & I2C serial EEPROM (automotive grade)
  MAX3050 CAN tranceiver
  MAX3110 SPI to UART/RS232
  Mot MC33399 LIN tranceiver
  2N3904 & MAX6605 temperature sensors on board
  on board serial to JTAG (no separate board)
  2 MAX7301 SPI to GPIO expander
  2 MAX6126 (4.096 & 2.048) precision reference (3pmm). (In addition to on chip references)
  MAX5491precision resistor divider
  32kHz and 8MHz crystals

## Slide 23: EV-Kit Description

## Slide 24: Software & Product Dev. Support
  Supported by the IAR Embedded Workbench - Integrated Development Environment:
    C/Embedded C compiler
    Assembler
    Linker
    Librarian
    Editor
    Project manager and debugger

## Slide 25: Strengths & Opportunities
Strength:
  MAXQ Core
  Design Expertise : Analog, Low power
  The right feature list
Opportunity:
  Market trends
  The right set of features

## Slide 26: Samples OCTOBER 2004

## Slide 27: Example Product Table
Part Number | DVDD | FVDD | ADC / DAC Resolution | VDDIO / AVDD | Max Speed | Temperature Range | Package | FLASH | RAM
MAXQ7653CAGN | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +125degC | 56QFN | 32kBytes | 1kByte
MAXQ7653BAGN | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +125degC | 56QFN | 64kBytes | 2kBytes
MAXQ7653AAGN | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +125degC | 56QFN | 128kBytes | 2kBytes
MAXQ7653CAGK | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +125degC | 68QFN | 32kBytes | 1kByte
MAXQ7653BAGK | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +125degC | 68QFN | 64kBytes | 2kBytes
MAXQ7653AAGK | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +125degC | 68QFN | 128kBytes | 2kBytes
MAXQ7653CEGN | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +85degC | 56QFN | 32kBytes | 1kByte
MAXQ7653BEGN | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +85degC | 56QFN | 64kBytes | 2kBytes
MAXQ7653AEGN | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +85degC | 56QFN | 128kBytes | 2kBytes
MAXQ7653CEGK | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +85degC | 68QFN | 32kBytes | 1kByte
MAXQ7653BEGK | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +85degC | 68QFN | 64kBytes | 2kBytes
MAXQ7653AEGK | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +2.7V to +3.6V | 8MHz | -40 to +85degC | 68QFN | 128kBytes | 2kBytes
MAXQ7654CAGN | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +125degC | 56QFN | 32kBytes | 1kByte
MAXQ7654BAGN | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +125degC | 56QFN | 64kBytes | 2kBytes
MAXQ7654AAGN | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +125degC | 56QFN | 128kBytes | 2kBytes
MAXQ7654CAGK | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +125degC | 68QFN | 32kBytes | 1kByte
MAXQ7654BAGK | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +125degC | 68QFN | 64kBytes | 2kBytes
MAXQ7654AAGK | +2.7V to +3.6V | +3.0V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +125degC | 68QFN | 128kBytes | 2kBytes
MAXQ7654CEGN | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +85degC | 56QFN | 32kBytes | 1kByte
MAXQ7654BEGN | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +85degC | 56QFN | 64kBytes | 2kBytes
MAXQ7654AEGN | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +85degC | 56QFN | 128kBytes | 2kBytes
MAXQ7654CEGK | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +85degC | 68QFN | 32kBytes | 1kByte
MAXQ7654BEGK | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +85degC | 68QFN | 64kBytes | 2kBytes
MAXQ7654AEGK | +2.7V to +3.6V | +2.7V to +3.6V | 12-bit / 12-bit | +4.75V to +5.25V | 8MHz | -40 to +85degC | 68QFN | 128kBytes | 2kBytes

## Slide 28: Contact Information
Business Management
    Anita Ganti
    Maxim SP&C Sunnyvale
    120 San Gabriel Dr.
    Sunnyvale, CA 94086
    408-530-6299
    anita_ganti@maximhq.com